## Slide 1: Overview of Ethernet Audio Networks
Attila Karamustafaoglu, 27.9.2007

## Slide 2: Contents
Introduction to Ethernet
EtherSound and Cobranet Ethernet Packets
Other Networks

## Slide 3: The “OSI Model“

## Slide 4: Ethernet Physical Layer Standards
Medium | 10MBit/s | 100MBit/s | 1GBit/s | 10GBit/s
Copper Coax or Twinax | 10BASE-5 10mm coax with vampire connector (1983) 10BASE-2 Thin coax cable | - | 1000BASE-CX* | -
Copper Twisted Pair | 10BASE-T | 100BASE-TX 100BASE-T2* (CAT3 with PAM Modulation) 100BASE-T4* (CAT3) | 1000BASE-T | 10GBASE-T (55m CAT6e 500MHz, 100m CAT6a 625MHz)
Optical | 10BASE-F | 100BASE-FX (FDDI, vertical or campus backbones) | 1000BASE-SX (horizontal fiber – low cost) 1000BASE-LX (vertical or campus backbones) | 10GBASE-LX4 10GBASE-SX4 10GBASE-SR 10GBASE-SW 10GBASE-LW 10GBASE-LR 10GBASE-ER 10GBASE-EW
* Standards without market success

## Slide 5: The Ethernet frame on the data link layer
 | Minimum Packet size | Maximum Packet size*
Overall size | 72 Bytes | 1526 Bytes
User Data | 46 Bytes | 1500 Bytes
Overhead in Bytes | 26 Bytes | 26 Bytes
Overhead in % | 36.1% | 1.7%
* Larger sizes possible with „Jumbo-Frames“

## Slide 6: On which layer to transport Audio
Layer | Advantages/Disadvantages | Examples
1 – physical layer | +Low overhead - Only point-to-point connections can be established with a guaranteed quality of service (QoS) (Ethernet hubs are useless) | AES-10 (MADI) AES-50 (SuperMAC) Aviom A-Net
2 – Data Link Layer (MAC Addressing) | + Audio can be distributed point-to-point and/or broadcast (Address FF:FF:FF:FF:FF:FF) using ethernet switches + low overhead + other traffic possible (but risky!) No routing over large networks and internet No point to multipoint | CobraNet Ethersound
3 – Network Layer (IP Addressing) | + flexible network topologies routing configurable + standard PC hardware High overhead Difficult sync extraction | AXIA Livewire
4 – Transport Layer (UDP or TCP/IP) Or higher | + Worldwide routing Low efficiency Difficult sync extraction, very high latency no Quality of Service | Internet Audio Streaming RTP

## Slide 7: Large or small packets for audio?
One Packet can carry between 15 and 500 audio samples at 24bit/48kHz
The transmission time is between 0.27 and 5.85 sample periods for a 100MBit/s network at 48kHz.
They can be used to transport:
one sample of multiple channels
multiple samples of one channel
a combination thereof
Small packets | Large Packets
High overhead | Low overhead
Low latency | High latency (about 6 samples for max. size)

## Slide 8: Assumed Packet structures of CobraNet and Ethersound
1
2
3
4
5
6
7
8
1
2
3
4
5
6
7
8
1
2
3
4
5
6
7
8
1
2
3
4
1
2
3
4
5
6
7
8
t(1)
t(2)
t(3)
t(n)
CobraNet 100Mbit/s
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
57
58
59
60
61
62
63
64
t(1)
Ethersound ES-100
8 channels (1 bundle) per frame
Multiple samples (ca. 50-100) in one frame and large buffers -> high latency
Up to four bundles per 100MBit/s cable possible -> flexibility
64 channels per frame -> low flexibility
One sample in one frame -> low latency
Bundle m
1
2
3
4
5
6
7
8
1
2
3
4
5
6
7
8
1
2
3
4
5
6
7
8
1
2
3
4
1
2
3
4
5
6
7
8
Bundle b
1
2
3
4
5
6
7
8
1
2
3
4
5
6
7
8
1
2
3
4
5
6
7
8
1
2
3
4
1
2
3
4
5
6
7
8
Bundle a

## Slide 9
Other networks with market weight
Optocore - 512 ch optical redundant ring, transporting also 100MBit/s data and Video - very popular in Germany
AES50 (SuperMAC) - based on 100MBit/s Ethernet 48ch links and proprietary routers - used by MIDAS XL8 but no other prominent integrators
Livewire - True IP-Audio Network for Broadcast Applications - Owned by Telos/Axia - Playout from standard PC Ethernet card possible - high channel counts >8ch per node never demonstrated
mLAN - IEEE-1394 daisy chains for audio and MIDI - Owned by Yamaha - Seems not to get much ground in the pro market

## Slide 10: Thank you!

## Slide 11: Resulting topologies for CobraNet
N1
N2
N3
N4
N5
Switch
N0
N1
N2
N4
Switch
N29
N30
N31
N32
Random but restricted networks possible with unicast bundles
Each node can receive or transmit a maximum of 4 bundles
Random Network
PA Distribution Network
Control PC
Control PC
Broadcast Bundles
Unicast Bundles

## Slide 12: Resulting topologies for Ethersound 1
N0
Daisy chain network with loopback
N1
N2
N3
N4
N5
N6
N7
N8
N0
Daisy chain network
N1
N2
N3
N4
N5
N6
N7
N8
N0
Redundant ring
N1
N2
N3
N4
N5
N6
N7
N8

## Slide 13: Resulting topologies for Ethersound 2
Star Topology
N0
N1
N2
N4
Switch
N29
N30
N31
N32
PA Distribution Network
Control PC
N1a
N1b

## Slide 14: CobraNet Overview
20 Bit resolution
Very high installed basis in live and install market
Implemented by BSS, Crown, QSC, BiAmp, Yamaha, Studer, Soundcraft…
Not suitable for many applications like monitoring due to it‘s large latency (5.33ms)
Redundant links possible, but (!) inactive link is not supervised -> rather useless
96 kHz, 24 Bit, or lower latencies such as 1.33ms or 2.66ms possible with different module firmware but with drawbacks (e.g. only 7 channels per bundle)
Gigabit standard is in a very early stage.

## Slide 15: CobraNet Discovery Tool

## Slide 16: Ethersound Overview
Becoming more and more important in live and broadcast markets
Implemented by Digigram, Auvitran, Innovason, Nexo, Yamaha, Allen & Heath, DiGico, Martin Audio, Studer, Soundcraft…
ES-Giga Gigabit standard is in a very early stage but has been demonstrated

## Slide 17: ES Control Software

## Slide 18
Summary
Both Ethersound and Cobranet are used in the market. Ethersound mostly in live and broadcast, Cobranet mostly in Live / Install.
Both have their technical drawbacks
Cost effective cabling and distributing is the main advantage of both network technologies