## Slide 1
The best digital protocol for bi-directional audio and data…?
BIAMP SYSTEMS
&
CobraNet

## Slide 2
The Pyramid of Networked Audio Systems
R e d u n d a n t N e t w o r k
Control & Surveillance System
Digital Audio Platform (DSP)
Control Devices
Alarm / Audio
Input Devices
Fire detectors / Sensing mic’s /
CD, DVD, MP3 Players, mics, instruments,…
Audia RCB devices /
3rd party controls via Logic
or Ethernet
daVinci/Audia Software !
AUDIA Flex CM !
Switches / CAT5
or FO cables
CobraNet (fixed latency !!)

## Slide 3
Redundant networks allow for automatic
“self healing” systems and can be monitored via several applications.
CobraNet (CM-1)is redundant too !
BIAMP SYSTEMS
&
CobraNet

## Slide 4: CobraNet Basics
Operates “over” Ethernet
Transported on bundles
  Basic network transmission unit
  Collection of audio channels
Notes: Like TCP/IP, CobraNet is transmitted “on top of” Ethernet.
They are not exclusive of each other.
(Bundles Slide)

## Slide 5: CobraNet Bundles
1 bundle may contain up to 8 channels of 48kHz, 20 bit audio
CM-1
  Transmit 4 bundles
  Receive 4 bundles
  Total of 64 audio channels
Notes: Each bundle carries a maximum of 8 channels of 48kHz, 20 bit audio.
(Bundle Numbers Slide)

## Slide 6: Bundle Numbers
0
  Empty
1-255
  Public multicast
256-65279
  Public unicast
65280-65535
  Private unicast
Notes: There are three types of CobraNet bundles. They are distinguishable by their bundle number.
Bundle 0 is special. It is the empty bundle.
Multicast – bundles allow more than one receiver
Multicast bundles must be used sparingly. More than four on a single LAN can cause bandwidth utilization issues.
Public – Unicast bundles accessible to any single receiver
Private – Unicast bundles accessible to a specified receiver
Audia software assigns private bundle numbers to the automatic CobraNet links
Audia can explicitly be set to transmit/receive on any other bundle number with the CobraNet blocks.
You might ask, how many bundles can be transported over a network.
(Network Capacity Slide)

## Slide 7
Redundant CobrNet network for Communication, Audio, Alarm and EVAC
Audio Network devices with CobraNet
Audio Network devices with CobraNet
By switching receipients bundle numbers (not TCP/IP or MAC adress), a lot of different zones can be adressed easily.... very nice and easy to program !

## Slide 8
CobraNet beneficials: We can talk to other manufacturers products via the same protocol ! We can share DSP power via CobraNet We can define the max. no. of channels, by creating a network with enough bandwith ! Max. no. of CobraNet links is kind of unlimited in a large system ! We will go further and use the data channel in CobraNet for bidirectional controls ! We can use it for sending/receiving audio signals within a network, which we could not do before (i.e. AEC via CobraNet) (Geographical solutions !)

## Slide 10
CobraNet beneficials: ...and we can look further into the future of Paging System solutions via CobraNet......

## Slide 11
Networked
Paging Stations
The newest addition to the AudiaFLEX family of products.
BIAMP SYSTEMS PRESENTS

## Slide 12: The Concept:
To seamlessly integrate a sophisticated
networked paging solution into the existing
AudiaFLEX CM platform.
This paging solution shall be able to
integrate with any existing CobraNet
enabled AudiaFLEX.

## Slide 13: Networked Paging Station:
The Networked Paging Station will
consist of a base station with a fixed
microphone, LCD display, and user controls

## Slide 14: Station Features:
LCD display:
Button selection
Zone status
Paging status
Network indication
Both CobraNet and Control over 1 port!
This station will plug into the CobraNet network only!
Rotary encoder for selection
Push to Talk/Latch switch
Optional 4 digit lockout for access control
External power supply and PoE capable

## Slide 15: NPS in Audia Software:
The Networked Paging Station has its
own unique input block within software.
Each Paging Station block can have up
to 32 “buttons”.
A button is what the user will select via the Networked
Paging Station’s interface to page into a set of zones.

## Slide 16: NPS in Audia Software:
Any number of Networked Paging Stations
may correspond to a particular Paging
Station block
All Network Paging Stations assigned to the particular
NPS block will all receive identical buttons.

## Slide 17: NPS in Audia Software:
The NPS-1 blocks tie to another new block:
the Page Zone Router

## Slide 18: NPS in Audia Software:
The Page Zone Router is where the
Paging Station block’s buttons are
are assigned to zone outputs.

## Slide 19: NPS in Audia Software:
Both the NPS-1 input block and the Page Zone Router also provide some logic indication:
CobraNet Network Indication
Microphone Functionality
If any Button has been pressed
If a specific Button has been pressed
If a specific zone is currently being paged

## Slide 20: System Features:
For one AudiaFLEX, you can have up to 16 paging stations active at one time through reserved CobraNet channels
-These are CobraNet channels set aside from what is available in Audia that can only then be used for paging stations
The Page Zone Router block can receive up to 32 NPS-1 blocks, routing up to 28 different zones in one AudiaFLEX.

## Slide 21: Paging in action:
If a user selects a button or multiple buttons, the LCD display will show if the zones within that button are available to be paged into.
If two Paging Stations attempt to page into a zone that they both have the same priority to. The first station to start wins.
Paging Stations that have a higher priority can override stations with less priority.

## Slide 22: Hospital Paging System:
How it will be done with Networked Paging Stations:

## Slide 23: Hospital Paging System:
Since multiple stations can be assigned to the same block we are reducing programming time, and overall DSP:

## Slide 24: How it would look with Networked Paging Stations!

## Slide 25
The best digital protocol for bi-directional audio and data…?
We believe it totally fulfills our needs…
and Gigabit CobraNet is coming…!
BIAMP SYSTEMS
&
CobraNet