## Slide 1: Ethernet Audio Video Bridging
Presentation for the Swiss AES Section
Attila Karamustafaoglu, 17. 3. 2009
Studer Professional Audio GmbH, CH-8105 Regensdorf

## Slide 2: Contents
Motivation for a new standard
Introduction into the standard and its sub-standards
Pros and cons
Applications
Questions

## Slide 3: Motivation for a new standard
Disadvantages of most current audio over Ethernet standards:
Signals can be transported either in broadcast or unicast mode:
- Broadcast occupies links with unneeded data
- Unicast requires same signals to be sent to multiple receivers
- Multicast is not possible
Mostly the standard is proprietary and supports either 100Mbit/s Ethernet or 1Gbit/s Ethernet
Multiple switch hops increase jitter and lead to indeterministic behavior
No prioritization of audio traffic over data traffic
Audio data only (no video)
If layer 3 (ip based, routable) is used, the latency and overhead is big
-> AVB eliminates all these disadvantages

## Slide 4: The three columns of the AVB standard
IEEE 802.1AS
Precision Time synchronization protocol (PTP)
Based on
IEEE 1588
IEEE 802.1Qat
Stream reservation protocol (SRP)
IEEE 802.1Qav
Forwarding and queuing of time-sensitive streams

## Slide 5: Basic principles of the AVB standard
A network consists of nodes and AVB bridges, like a network of e.g. PCs and Ethernet switches
Time synchronization (PTP) makes sure that all nodes in the network are synchronous to the same time.
Audio and video data is packed into streams.
Nodes can request streams from other nodes.
The stream reservation protocol (SRP) makes sure that the streams are routed through the network and the required bandwidth in all AVB bridges is reserved.
If a stream is consumed by several nodes, it is duplicated in the AVB bridges along the path.
All nodes play out the streams synchronously, no matter what distance to the sender.

## Slide 6: Time synchronization – best master clock algorithm
Node 1
Class 2
AVB Bridge
AVB Bridge
AVB Bridge
Node 2
Class 1
Node 3
Class 1
Node 4
Class 2
Node 6
Class 1
Node 5
Class 2
Node 7
Class 3
Each node advertizes its local clock’s quality class
The nodes with the best clock class elect a grandmaster amongst them
If the master disappears, a new election process will be initiated automatically
A Priority attribute field allows manual selection of the grandmaster

## Slide 7: Time synchronization – Drift compensation
Sync() packet is very small for minimum transmission jitter
It is sent regularly (about every 10ms) by the master
Follow_up message tells in retrospective the time when the sync() message was sent
Differences between sync packets allow the receivers to compensate the drift of their clocks
Sync()
Follow_up(t0)
Sync()
Follow_up(t1)
Sync()
Follow_up(t2)
Sync()
Follow_up(t3)
Master
Slave
t
t

## Slide 8: Time synchronization – Delay compensation
Slave requests master’s current time
By measuring the delay until the answer arrives back, it can interpolate the one-way transmission delay
Considering this it can set its own clock to the same time as the master’s
Delay_req()
Delay_resp(t1)
Master
Slave
t master
t1
t0
t2
Delay_req()
Delay_resp(t1)
t4
t3
t5
t slave

## Slide 9: Time stamping of PTP packets containing 802.1AS Ethertypes
Timestamps are inserted by the timestamp engine which intercepts the data traffic on the MII level. This minimizes network jitter.

## Slide 10: Time stamping at the switch
2 versions exist
1. Boundary clock (IEEE-1588): Switch acts as a node and maintains an own clock. Sync packets passing the switch are re-timestamped with the switch’s clock information.
2. Transparent clock (IEEE-1588 Version 2): Switch modifies the timestamps with the delay the packet gets when passing through the switch
Transparent clock allows the nodes to recover faster when the network topology is reconfigured.

## Slide 11: Break

## Slide 12: Presentation Time
For each audio/video packet, a presentation time is specified by the sender. It has a fixed offset to the sampling time which is a (user-definable) constant. The default value for this constant is 2ms, resulting in an overall network latency of 2ms.
Packet k (sampled at 1h15’47“355253415ns)
„play me at
1h15’47“357253415ns“
A/V Data
„play me at
1h15’47“357378415ns“
A/V Data
„play me at
1h15’47“357503415ns“
A/V Data
Packet k+1 (sampled at 1h15’47“355378415ns)
Packet k+2 (sampled at 1h15’47“355503415ns)

## Slide 13: Protocol encapsulation

## Slide 14: IEC-61883
IEC-61883 defines the packing of Audio/Video data in IEEE1394 (aka Firewire) and is reused in AVB.
The standard is divided into several subparts*:
IEC-61883-1: General
IEC-61883-2: SD-VCR Data Transmission
IEC-61883-4: MPEG2-TS Data Transmission
IEC-61883-6: Audio and Music Data Transmission Protocol
IEC-61883-7: Satellite TV MPEG
IEC-61883-8: Bt.601/656 raw video
IIDC Uncompressed Industrial Cameras
* Some 61883 subparts are not supported in AVB

## Slide 15: AVB Media Clock
At the local end of an AVB node, the A/V data is clocked out with the media clock (e.g. 48kHz for audio).
The media clock is not derived from the PTP based system clock but from the received stream.
This allows streams to be asynchronous to each other.
Stream sources can just use their own local clock which makes the node implementation cost-effective.

## Slide 16: A little bit of math
At 100Mbit/s a full size Ethernet packet has a transmission time of 122.4us
What is the minimum latency?
Transmission of one Ethernet packet takes 122.4us
AVB specifies that 7 hops are allowed, so the transmission time over all hops is ca. 0.85ms (cut-through switching not assumed)
Allowing for some margin for buffering at the end nodes and queuing and transfer time within the AVB bridges, AVB specifies a default value of 2ms.
What is the maximum channel count per stream?
In 122.4us, 5.875 audio samples are taken at 48kHz, so the next non fractional number of samples have to fit in to a packet: 6
This corresponds to a packet rate of 8 kHz.
One packet can carry 367 samples, which results in 6 samples of 61 channels.

## Slide 17: Pros/cons
+ “standard Ethernet” technology can be used
+ 100Mbit/s and 1Gbit/s standard can be mixed
+ Robust clocking scheme
+ open standard
+ Media can be converted between optical/electrical to fit the need of the application
- Switches (AVB bridges) have to support the protocol, which makes them more expensive than standard Ethernet switches.
- Audio channels have to be “bundled” into streams which can not be split by AVB bridges
- Default latency of 2ms is at the upper limit for some professional applications (but the setting could be lowered in controlled environments)
- Redundancy not clearly defined
- 100Mbit/s support pushes up the network latency
- 1Gbit/s is not sufficient for uncompressed HD video signals

## Slide 18: Applications - Consumer
The consumer industry is the main driver for AVB:
Vision:
All audio/video devices only have an AVB connector (or wireless AVB receiver) instead of a multitude of cinch, HDMI, Toslink, S-VHS etc. connectors (imagine an AVB receiver)
A home has an AVB network backbone which runs all kinds of data such as audio/video and standard data (Ethernet, Internet, VoIP).

## Slide 19: Applications - Pro
AVB allows reusing current twisted pair / fiber cabling infrastructures.
Sharing of I/O is possible with stream multicast.
7 hops allows some flexibility but could be restricting. In large systems, the network topology design needs careful consideration.
AVB will probably not displace SDI for video transport (3Gbit/s on one coax cable) in the professional domain. As an SDI video link can transport 16 audio channels as ancillary data, SDI router networks will fulfill the task of routing the audio data.

## Slide 20: Thank you