## Slide 1
Dante Media Networking
1
Kieran Walsh
Senior Technical Solutions Manager- EMEA

## Slide 2: About Audinate
The leading developer of media networking technology with core competencies in media networking, time synchronization techniques, and zero-network configuration
Audinate has pioneered an open standards based approach to develop high quality audio and media over standard TCP/IP computer networks
Our vision is to revolutionize the way that AV systems are connected. We do this by transporting high quality media over standard IT networks
We are not just networking implementers…
We are the inventors who are leading the way

## Slide 3: Audinate…leading the way
First media networking solution to implement IEEE1588 for ultra accurate clock synchronization.
First Pro AV networking solution to fully exploit gigabit and QoS in Ethernet switches.
First AV solution to implement label based routing to simplify complex network configuration.
First networking solution to enable a common shared network for audio, control and data traffic.
First company to implement full glitch free redundancy.

## Slide 4: Over 45 licensed manufacturers and growing

## Slide 5: Audinate’s markets today…
Broadcast
AV systems
Recording
Post Production
Broadcast Systems
Public Address
Conference Systems
Rail
Airports
Voice Alarm
Evacuation Systems
Boardrooms
Broadcast
AV systems
Recording
Post Production
Broadcast Systems
Installed Systems
Stadiums
Auditoriums
House of Worship
Universities
Corporate Buildings
Casinos
Professional
AV systems
Live Concerts Venues
Live Events
Music Instrument
Equipment

## Slide 6
Stevie Wonder
Audinate in Use: Sound Reinforcement
“Dante’s easy to configure text based
channel labeling and routing
helped smooth the transition
between acts.”
Paul McCartney
“Dante sounded significantly better
than other digital formats and
definitely sounded better than long
runs of analog cable."

## Slide 7: Dante in installed sound
“Dante network system connected 2 million watts of amplifiers”
  “With the Dante Virtual Soundcard, we
  have a complete recording solution”
2010 Winter Olympics
Broadway, NYC- West End, London

## Slide 8: Dante in Stadiums
Twinkenhem Stadium
London, England
Lord’s Cricket Ground
London, England
Voice Evacuation Audio Alarm and Public Address Systems

## Slide 9
Network Evolution

## Slide 10: Early audio networking over Ethernet approaches
Used Ethernet, but not IP
Typically closed non-standard systems
“Layer 2” only – no higher network functionality
Solved problems of that time period but imposed limitations
  Latency or scalability tradeoffs
  Could not easily support data, voice and control

## Slide 11: Early audio over Ethernet limitations
100Mbps networks
High latency (CobraNet)
Complex to set up
  “Bundles” of channels difficult to manage, channels, or route
Multiple VLANs required to break network into 100Mbps parts
No way to interface directly with PCs

## Slide 12: Convergence of A/V & IT Networks
Huge, standards-driven industry
Ubiquitous, fast, cost effective
Incredibly reliable
Deep integration with computer applications
Using modern networking technology keeps you future-proof!

## Slide 13: AVnu Alliance™
AVnu Alliance is an alliance dedicated to the advancement of professional-quality audio video by promoting the adoption of the IEEE 802.1 Audio Video Bridging (AVB), and the related IEEE 1722 and IEEE 1733 tranports.
Member companies include Analog Devices, Audinate, Avid, Bosch, Broadcom, Cisco, Extron, Intel, Harman, Loud, Marvell, Meyer Sound, Peavey, PreSonus, Sennheiser, Shure, TC Group, Xilinx and Yamaha.

## Slide 14: AVB Clouds

## Slide 15: AVB Transport Protocols – IEEE1722
IEEE1722 is new transport protocol which runs entirely at Layer 2
Firewire/IEEE1394 frames are encapsulated into Ethernet frames
  802.1Qat is used to reserve bandwidth
  Ethernet packets use 802.1Q headers with priority
IEEE1722 uses 802.1as to provide timestamps for synchronization
IEEE1722 is not routable across subnets

## Slide 16: AVB Transport Protocols – IEEE1733
IEEE1733 is an extension to the Real-time Transport Control Protocol (RTCP)
  Supports AVB 802.1as clock synchronization
RTP is a well established media transport protocol
  RTP use in VoIP, video conferencing and IPTV
RTP streams can easily use AVB QoS services:
  Reserve bandwidth using 802.1Qat
  Mark packets with 802.1Q priorities
RTP can be routed across subnets
1733 supports 33% more channels over link

## Slide 17
Migrating to AVB

## Slide 18: Dante- Making Digital Networking Easy
Dante offers a complete network solution
Dante self discovery and label based routing.
Simplified ease of use and set up time.
Dante’s architecture is built on standard Internet Protocols – not just Ethernet
AVB Ready- Built on global networking standards including IEEE 802.3, UDP/IP and IEEE1588

## Slide 19
Network Configuration
Automatic discovery
of Dante enabled devices
on the network.
Simple label-based routing. No “magic numbers” or MAC addresses to learn
Easily to make changes
to systems without touching
equipment.
Notes: 19

## Slide 20: Dante Virtual Soundcard
PC networked implementation that turns your audio applications into network audio applications with Dante Virtual Soundcard
Dante enables your PC/Mac
Record, playback, process networked digital-audio with no loss of quality
No soundcard hardware needed
Just use the Ethernet built-in to your
PC or MAC
Virtual Soundcard appears as a
multichannel ASIO or Core Audio device

## Slide 21: Migration path of Dante to Dante/AVB
100Mbps/1Gbps Cat5e/Fiber
Quality of Service (QoS) DSCP/VoIP
Clock Sync IEEE1588 PTP
Audio Transport
ATP
Dante Today
Dante AVB Layer 2 or Layer 3
Dante Transport

## Slide 22: Migration path of Dante to Dante/AVB
100Mbps/1Gbps Cat5e/Fiber
Quality of Service (QoS) DSCP/VoIP
Clock Sync IEEE1588 PTP
Audio Transport
ATP
Dante Today
Dante AVB Layer 2 or Layer 3
Simple Signal Routing
Network Monitoring
PC/Mac Dante Virtual Soundcard
Glitch-Free
Redundancy
Performance Monitoring
Latency Management
Device and Channel Discovery
Automatic Configuration
Dante solution today

## Slide 23: Migration path of Dante to Dante/AVB
100Mbps/1Gbps Cat5e/Fiber
Quality of Service (QoS) DSCP/VoIP
Clock Sync IEEE1588 PTP
Audio Transport
ATP
Dante Today
100Mbps/1Gbps Cat5e/Fiber
Quality of Service (QoS) DSCP/VoIP / 802.1Qav / 802.1Qat
Clock Sync IEEE1588 PTP / 802.1as
Audio Transport
ATP / 1722 / 1733
Dante AVB Layer 2 or Layer 3
Simple Signal Routing
Network Monitoring
PC/Mac Dante Virtual Soundcard
Glitch-Free
Redundancy
Performance Monitoring
Latency Management
Device and Channel Discovery
Automatic Configuration
Dante solution today
AVB

## Slide 24: Migration path of Dante to Dante/AVB
100Mbps/1Gbps Cat5e/Fiber
Quality of Service (QoS) DSCP/VoIP
Clock Sync IEEE1588 PTP
Audio Transport
ATP
Dante Today
100Mbps/1Gbps Cat5e/Fiber
Quality of Service (QoS) DSCP/VoIP / 802.1Qav / 802.1Qat
Clock Sync IEEE1588 PTP / 802.1as
Audio Transport
ATP / 1722 / 1733
Dante AVB Layer 2 or Layer 3
Simple Signal Routing
Network Monitoring
PC/Mac Dante Virtual Soundcard
Glitch-Free
Redundancy
Performance Monitoring
Latency Management
Device and Channel Discovery
Automatic Configuration
Dante solution today
AVB
How to you configure network?
How do you discover devices?
How to you set up routing?
Notes: We haven’t said much about Audinate’s Dante yet. Audinate provides a complete stack to multiple manufacturers with whom we partner, implementing a complete standards-based solution.
This chart illustrates how Dante fits into AVB.
Of course Dante has been designed in a pre-AVB world, and we have taken advantage of the latest advancements in IT networking to provide very high performance transport of media streams. AVB helps to simplify the deployment of Dante systems just as it promises to do for everyone else.
On the left hand side you can see the elements that comprise the Dante system, from all the low level functions like clock sync and transport to the upper level features that complete the system – automatic device discovery and configuration, signal routing, management of latency at individual devices, redundancy, performance and network monitoring and our virtual implementation of Dante for Windows and Macintosh. This last item is the Dante Virtual Soundcard, and turns any PC into a fully bidirectional Dante node on your network for media recording and playback.
At this point in time, AVB seeks to standardize critical functionality at only the lower levels of this model – the upper levels will be filled out by different manufacturers in their own designs for hardware and software.
The red text on the right hand side illustrates the changes to the Dante implementation that AVB requires; we’ll be adding compliance with AVB Core Services and Transport, but this does not in any way interfere with or change our upper level functions. Dante will continue to be able to work in non-AVB as well as AVB-compliant networks.
The best part? All Dante-enabled devices can be updated to AVB compliance with a simple firmware update, and so Dante equipment purchased and in use today can be made “AVB aware” as soon as it is needed.

## Slide 25: Migration path of Dante to Dante/AVB
100Mbps/1Gbps Cat5e/Fiber
Quality of Service (QoS) DSCP/VoIP
Clock Sync IEEE1588 PTP
Audio Transport
ATP
Dante Today
100Mbps/1Gbps Cat5e/Fiber
Quality of Service (QoS) DSCP/VoIP / 802.1Qav / 802.1Qat
Clock Sync IEEE1588 PTP / 802.1as
Audio Transport
ATP / 1722 / 1733
Dante AVB Layer 2 or Layer 3
Simple Signal Routing
Network Monitoring
PC/Mac Dante Virtual Soundcard
Glitch-Free
Redundancy
Performance Monitoring
Latency Management
Device and Channel Discovery
Automatic Configuration
Dante solution today
Simple Signal Routing
Network Monitoring
PC/Mac Dante Virtual Soundcard
Glitch-Free
Redundancy
Performance Monitoring
Latency Management
Device and Channel Discovery
Automatic Configuration
Dante AVB
AVB

## Slide 26: AVB and network switch market
Broadcom and Marvel shipping “AVB capable HW chips”
Firmware development is still required by switch vendor.
One switch announced
No major switch vendors have yet to announce support.
Just like we saw in 3G networks, or 802.11 WiFi… you need backward compatibility.
Think about a transition strategy when it makes sense.
Audinate offers a safe migration path to AVB

## Slide 27: Summary AVB
AVB is an Audio over IP solution
AVB improves QoS in switches
AVB requires specialized switches
Major enterprise switch suppliers have yet to announce an AVB supported switch
Recommend designers have flexibility when implementing AVB and have a solution that will work with or without AVB switches
Dante “Futureproofs” designs

## Slide 28
Dante- Leading the Way
www.audinate.com