## Slide 1
Active Velocity Acoustic Absorber

## Slide 2: Why is the AVAA necessary
The combination of reverb during recording and during reproduction must not exceed the reverb desired by the author of the acoustic message.
total perceived reverb
reverb of reproduction room
reverb recorded at distance < acoustic radius
(sub-critical distance)
time
SPL

## Slide 3: Why is the AVAA necessary
In a closed space, stationary waves can occur due to wall reflections.
A simple “axial mode” is a reverberation where the room’s dimensions (L) contain an integer number of half wave length (l/2).
wave acoustic velocity and wave acoustic pressure
On a wall, the acoustic pressure is maximal and acoustic velocity minimal.
L = (l/2)
L = 2(l/2)
L = 3(l/2 )
L
1st
2nd
3rd
pac = 0
pac = 0
pac
vac

## Slide 4: Why is the AVAA necessary
Instant superposition of modal pressures create, at one frequency, the well know maximal and minimal acoustic pressure, depending of our position in the room:
  pressure “peaks” or maxima create “keynote”,
  pressure “nulls” or minima reduce homogeneity.
  Both are causes of errors for the sound engineer.
microphone at 3/5 of the length of the room, L = 5 m
L

## Slide 5: Processes
EQ
Bass-trap
Noise cancelling
Anti-wall

## Slide 6: Processes
A microphone measures the acoustic pressure in front of an fabric with specific acoustic resistance
A electronic treatment converts this pressure into the resulting acoustic velocity through the fabric
The transducer's acoustic velocity is set to achieve zero acoustic pressure behind the fabric, i.e. in the “silent chamber”.
acoustic resistance
closed volume
silent chamber: Pac=0
A wall transforms the energy of the acoustic velocity into energy of acoustic pressure
The AVAA converts energy of the acoustic pressure into energy of velocity: we can call it an “wall-suppression”.
Pressure to Velocity conversion

## Slide 7: Prototypes and trials
For testing, 4 AVAA were positioned in the corners on the floor of the studio.

## Slide 8: Prototypes and trials
The AVAA, smaller than 50 dm3,…
…is compared to a bass trap of over 500 dm3.

## Slide 9: Prototypes and trials
Absorbing wall with bass trap
Absorbing wall alone
Absorbing wall with AVAA

## Slide 10: Auditory perception
A specific mode influences the auditory perception in time, frequency and space.
SPL
t
SPL
f
Time:
the pulse is extended.
Frequency:
pressure “peaks” create “keynote”, pressure “nulls” reduce homogeneity.
Space:
sound is perceived as a hum coming from everywhere and nowhere.

## Slide 11: Auditory perception
Listening close to the AVAA allows to confirm that no noise is emitted
To not be dominant, the extinction time of the natural modes must be similar to the reverberation time
An equalizer, although efficient only on the reproductive system, can also help other phenomena than the standing waves

## Slide 12: Auditory perception
Thank you for your attention