## Slide 1: Electroacoustic absorbers low frequency absorption by hybrid sensor/shunt-based impedance control
Dr. Hervé Lissek, Dr. Sami Karkar, Etienne Rivet (EPFL)
WARNING:
all sounds in this slideshow should be listened to with a subwoofer or (good) headphones.

## Slide 2: Outline
Context: room modes in the low-frequency range
Presentation of the Electroacoustic Absorber prototype
Design Methodology for room modal damping
Experimental assessment: modal damping in rooms

## Slide 3: Context

## Slide 4: Context
Room modes characterization: standing waves
   uneven spatial distribution of sound energy

## Slide 5: Context
Room modes characterization: frequency response
  dominated by strong peaks (resonances) and dips (anti-resonances)
Im(pk): resonance frequency
Re(pk): damping

## Slide 6: Context
Room modes characterization: modal decay time
   sustain at the various resonance frequencies once the source stops
   definition of MT60 – may strongly vary with frequency

## Slide 7: Problem(s)
Low-frequency noise issue

## Slide 8: Problem(s)
Music rendering issue in the low-frequency range

## Slide 9: Problem(s)
State of the art sound absorbers
totally inefficient in the LF range (see /4 rule)
Porous materials
Helmholtz resonators
Panel absorbers
absorption
BF

## Slide 10: Problem(s)
State of the art sound absorbers
bass-traps (membrane absorbers)
Efficient LF narrow-band (1 resonance frequency) sound absorbers
e-traps (active bass traps)
Efficient on 2 (adjustable) resonance frequencies
E-trap

## Slide 11: Electroacoustic Absorbers presentation

## Slide 12: Electroacoustic absorbers
Development of an active sound absorption solution with >0.83 along the range [20 - 200Hz]
Based on actuated membranes (loudspeakers) used as a membrane absorbers
Evaluation in reverberant conditions, focusing on low-frequency sound «equalization»
H. Lissek, R. Boulandet, and R. Fleury, “Electroacoustic absorbers: bridging the gap between shunt loudspeakers and active sound absorption”, J. Acoust. Soc. Am., 129(5), 2968-2978, (2011).

## Slide 13: Electroacoustic absorbers
Parameter | Description | Value | Unit
Mms | Moving mass | 14.7 | g
Rms | Mechanical resistance | 1.31 | N.s.m-1
Cms | Mechanical compliance | 242.3 | mm.N-1
Sd | Membrane surface | 151 | cm2
Bl | Force factor | 6.85 | N.A-1
Vb | Cabinet volume | 10 | dm3
r | Air mass density | 1.2 | kg/m3
c | Sound celerity in air | 344 | m.s-1
pt
v
pi

## Slide 14: Electroacoustic absorbers
The desired acoustic impedance Zat can be assigned by identifying the controller transfer function:
pt
v
pi
Qp(w)
Objective:
force the membrane to behave as a given acoustic impedance Zat
Effective acoustic impedance of the membrane

## Slide 15: Electroacoustic absorbers
Implementation in the prototype
Voltage-driven current amplifier
Filter implemented on a DSP platform
DSP

## Slide 16: Electroacoustic absorbers
ISO 10534-2 : acoustic impedance measurement technique
Acoustic impedance
Absorption coefficient
DSP

## Slide 17: Design Methodology for room modal damping

## Slide 18: 1. FEM simulation
Eigenfrequency study with Comsol Multiphysics
  Room
    CAD of the targeted room
    Define a given uniform real acoustic resistance Rwall for walls to fit with measurements
  Absorbers
    Same acoustic resistance Ra on all diaphragms
result: eigenfrequencies in [20 – 100 Hz]
Eigenvalues  modal decay times
Rwall
Ra

## Slide 19: 2. Optimal acoustic resistance
Changing the value of resistance Ra
for each mode, find the minimal value of MT60
translate as a frequency-dependant resistance
zoom

## Slide 20: 2. Optimal acoustic resistance
Changing the value of resistance Ra
for each mode, find the minimal value of MT60
translate as a frequency-dependant resistance

## Slide 21: 2. Optimal acoustic resistance
Changing the value of resistance Ra
for each mode, find the minimal value of MT60
translate as a frequency-dependant resistance Ra(f)

## Slide 22: 3. Impedance specification
The function Ra(f) serve as a specification for the electroacoustic absorbers impedance Zat(f)=Rat(f)+iwXat(f)

## Slide 23: 4. Implementation
Implementation in the prototype
Voltage-driven current amplifier
Filter implemented on a DSP platform
DSP

## Slide 24: Experimental validation of room modes damping

## Slide 25: Experimental assessment
4x4 electroacoustic absorbers prototypes
(total surface = 16x151 cm2 = 0.24 m2)
In a reverberant chamber of 226.9 m2
 evaluation of room modal damping

## Slide 26: Experimental assessment
Frequency response without and with absorbers
   identify individual room modes
   assess damping performance on peaks and dips amplitudes
Modal decay times without and with absorbers
   assess damping performance in the time domain
Recording of music rendering, without and with absorbers
   listen to the effect on music rendering
Recording of kick drum, without and with absorbers
   listen to the effect on acoustic music playing

## Slide 27: Experimental setup
Hardware
Recorders/analyzers
  B&K Pulse (frequency responses)
    frequency resolution: 31.5 mHz
  M-Audio M-Track 8 soundcard (recordings)
Microphones
Sources
Facility (reverberant chamber, V=215.6 m3, S=226.9 m2)
  Subwoofer
  Kick drum
  (Pearl Export)
  PCB 130D20
  (frequency responses)
  Beyerdynamic M101 N
  (recordings)
Supplementary
panel absorber
4 electroacoustic absorbers
at the 4 room corners
7 microphone positions

## Slide 28: 1. Frequency response
(blue: «Hardwalls», red: «Absorbers»)

## Slide 29: 1. Frequency response
Modal damping (dB)

## Slide 30: 2. Modal decay time
Mode 8 – waveforms
(hardwalls : 52.78 Hz - absorbers : 52.72 Hz)
Mode 8 - echograms
(hardwalls : 52.78 Hz - absorbers : 52.72 Hz)

## Slide 31: 2. Modal decay time
1/6MT10
1/3MT20
1/2MT30

## Slide 32: 2. Modal decay time

## Slide 33: 2. Modal decay time

## Slide 34: 3. Music rendering
Peggy Lee «Fever»
White Stripes «7 nation army»
Hardwalls (mic 5)
Absorbers (mic 5)
Hardwalls (mic 5)
Absorbers (mic 5)
What’s this tune?
What’s this tune?

## Slide 35: 4. Kick drum
Waveforms
Echograms
Hardwalls (mic 1)
Absorbers (mic 1)

## Slide 36: Conclusions
4 electroacoustic absorbers prototypes achieve efficient room mode damping in the reverberant chamber
  Max damping: 12.2 dB @ 58 Hz,
  Global damping: 8 dB over [20 – 100 Hz],
  Max modal decay time reduction: 85% @ 58 Hz
  (from 20 s down to 3 s),
for a total absorber surface representing only 0.1% of the whole room walls surface

## Slide 37: Conclusions
Most recent results (August 2015)
as per December 2014
20 dB
8dB
70 dB
30 dB
40 dB
65 dB

## Slide 38: Thank you for your attention
This work has been supported by the Swiss Commission for Technology and Innovation (CTI), under the project INTERACTS, agreement number: 14220.1 PFNM-NM.
e-mail: herve.lissek@epfl.ch